## Slide 6
GOOD NEWS FOR MILLDRILL OWNERS – R690 EACH

## Slide 7
Pepper Mills For Africa (Pty) Ltd
Introducing the
The Barista CrushGrind
Coffee Grinding Mechanism
Milling Gourmet Coffee
for the
Connoisseur

## Slide 8
Safety First – Always work between centre’s and observe all safety rules
If your lathe starts to shudder dive for cover –
switch off later (Slaan dekking!)

## Slide 9
With approval of Frans Gericke

## Slide 10
Target

## Slide 11
140mm x 80mm x80mm

## Slide 12
Turn tenons on both sides of blank to fit your chuck

## Slide 13
Drill 25mm hole right through the blank (Turn around if needed)

## Slide 14
Use your MillDrill (extended to 46mm) to drill to maximum depth
If you don’t have one widen the whole to 46mm with skew

## Slide 15
Done! Test with mechanism to fit loosely

## Slide 16
Steady tailstock in preparation for design

## Slide 18
Design of your choice “Coffee Pot” style

## Slide 19
Turn around to remove tenon not needed anymore

## Slide 20
Remove tenon safely

## Slide 21
Start fitting top >65mm

## Slide 22
Fitted snugly for a lady to remove

## Slide 23
Finish “Coffee Pot” design

## Slide 24
Lay out mechanism. Top to just protrude.
Mark middle of bottom section of mechanism where ceramic frame is

## Slide 25
Design grooves to be burnt
Marked groove

## Slide 26
Burn grooves with wire

## Slide 27
Sand (Abranet) 100 to 400 grid
Be careful not to over sand the
Area where the cap fits!!

## Slide 28
Use MillDrill to drill 46mm
right trough coffee grinder
If you don’t have a MillDrill use a skew

## Slide 29
Done – Sanded inside

## Slide 30
Shop made “Jam Chuck” 46mm tight fit

## Slide 31
Stabilize with revolving tailstock and remove tenon

## Slide 32
Remove tenon carefully

## Slide 33
Stabilize with “dummy” revolving tailstock inside

## Slide 34
Sand sharp edge for lady’s fingers

## Slide 35
Apply three layers of 50% sanding sealer
and 50% thinners mix – do not spin on!

## Slide 36
Apply same mix inside

## Slide 37
Fitting the mechanism

## Slide 38
Push mechanism in till it protrudes slightly to fit top as per next slide

## Slide 39
Lid fitting precisely over protruding mechanism stem

## Slide 40
Drill small hole till drill touches ceramic on line previously marked

## Slide 41
Press pin into hole to lock mechanism from moving
(Both sides if you wish)

## Slide 42
“Jam chuck” both sides to reburn grooves – to hide pin hole(s)

## Slide 43
Re-burn grooves

## Slide 44
Lightly touch Carnauba and Bee wax mix on polishing buff

## Slide 45
Buff

## Slide 46
Voila! Ready for the market – Sell at about R890 t0 R990
One free for every 10 bought
Cost of mechanism, handle and lid = R490

## Slide 47: THANK YOU!!
Piet and Charlie